## Slide 1: DSD Final Project Presentation
Group 8
Member: 陳柏帆 洪鈺萌 林志皓

## Slide 2: Contents
MIPS pipeline (baseline)
Cache design
Extention1 -- Branch Prediction
Extention2 -- Tow Level Cache
Extention3 -- Multiplication & Division

## Slide 3: 1.
MIPS Pipeline

## Slide 4: structure
Hand-drawn by
柏帆

## Slide 5: Instruction Fetch
Select next Instruction address
(jump/ branch/ PC+4)
When next address is not PC+4 , we set a “FLUSH”
(32’b0 for instruction)

## Slide 6: Instruction Decode
Control unit
Forwarding Unit
Determine whether Branch or not

## Slide 7: EX, MEM, WB
Select the data to be forward in MEM stage (from ALU or memory)
 Simplified forwarding unit

## Slide 8: 2.
Cache

## Slide 9: Structure
Direct-map( 4 words * 8 block)
Write-back
Valid bit (no dirty bit)
Valid bit 1 bit | Tag 25 bits | DATA 1 32 bits | DATA 2 32 bits | DATA 3 32 bits | DATA 4 32 bits
A block

## Slide 10: Finite State Machine
Only 3 states !
If hit, processor can get data from cache in the cycle of request
 Reduce total cycle
Read from
memory
Idle
Write
Back
Ready
Read miss
& valid
Not ready
Write or Read hit
Not ready
Ready
Need to
Write Back

## Slide 11: Baseline Performance
Cell Area : 284158
Execution Time : 9960.75 (ns)
AT rate : 2830426799

## Slide 12: 3.
Extention –
Branch Prediction

## Slide 13: Finite State Machine
Initially, the IDLE state is Strongly Not Taken
If prediction wrongly two times in a row, the state will go to Taken
Weakly
Not Taken
Strongly
Not Taken
Weakly
Taken
Strongly
Taken

## Slide 14: Overall Circuit

## Slide 15: Result
Cannot predict two successive branch instructions effectively
1234568

## Slide 16: 4.
Extention –
Two Level Cache

## Slide 17: Implementation Details
Separate 2 L2 caches for I cache & D cache
Direct Map
4 words/block, total 64 blocks(entries)
FSM: 3 state
Valid 1 bit | Tag 22 bits | Data 128 bits

## Slide 18: Result

## Slide 19: 5.
Extention –
Multiplication & Division

## Slide 20: Implementation Details
Iterative, stall 32 cycles for each Multiplication/Division Instruction
Record the position of Add/Subtract with Counter,
Thus determine when to stop “stalling”
Correctness Verification :
Check data in D cache with monitoring nWave
Add some negative number for testing

## Slide 21: Result
Numbers to be Multiplication/Division | -25 -3 | -25 3 | 25 -3
Multiplication |  |  | 
Division |  |  |